## Slide 1: Saving Energy & Money
James Oswald
Member Cosby Golf Club
Member Institute of Power Engineers

## Slide 2: Contents
Heating Clubhouse
Electrical Clubhouse
Greens shed
Cost & Savings

## Slide 3: Clubhouse heat

## Slide 4: Measure clubhouse temperature
Measured room temperatures
Members turn everything to maximum or off
Stuck radiator valves
Broken heater (nobody checks)

## Slide 5: Clubhouse electricity

## Slide 6: Clubhouse electricity
Read meter every hour
Peak during sunshine
  Peak power 19kW
  Install a 30kW system
  Batteries are optional
    Costly & space
    More panels may be better

## Slide 7: Clubhouse PV
Cost £1000/ kW installed
30kW system costs £30000
Battery or not?
  I suggest not – peak at midday
  Spend money on more panels
  They will advise battery
  Can divert power to hot water
2026 electricity price ~30p/kWh

## Slide 8: Clubhouse PV - 14th June 2025, cloudy
Grid imports (blue
Grid
PV

## Slide 9: Clubhouse PV result
Peak power is reduced

## Slide 10: Clubhouse Savings
Savings from:
  Solar panel
  LED lights
  Air conditioning unit in the pro shop

## Slide 11: Greens shed

## Slide 12: Greens shed
LED
Solar Panels
Air con heating/cooling

## Slide 13: Cosby Greens Shed
Calor gas heating before
Air con after

## Slide 14: LED
Versus 6200 lumens fluorescent 70W
Lumens 5150 lumens LED, 43W

## Slide 15: Recommendations
Heating
  Inspect system and measure temperatures
Electrical
  Make a list all electrical appliances – asses £
  Install LED lights throughout
  Install air con for heating
    Don’t use electric direct heaters
Solar PV panels
  Measure consumption of clubhouse and correctly size
Replace old refrigeration for cellar